## Slide 1
WHAT AFFECTS CURRENT?

## Slide 2
PROJECT ACTIVITY
For teachers (please view this slide in SLIDE SHOW mode to make the links clickable) —
1. Please click here to read p20 from the 3. Modelling section of the EEF Improving Secondary Science Guidance Report 2. Please follow this Link to answer the questions below. a. (Multiple choice) How familiar were you already with the Focus Action Reflection (FAR) approach? b. (Optional) Please share any examples/ideas that you have for ensuring that your pupils are familiar with the underlying idea that an intended model is based on (NB these ideas do not have to be for Yr7/8 electric circuits).

## Slide 3
NEED TO KNOW
You will need — | Your students will need — | Additional information —
This presentation DEMO: 4m length of rope, tied in a loop | Worksheet | Additional information is provided in the notes for some slides and in the Lesson Plan.
Notes: This slide contains everything you need to know to prepare for the lesson.

## Slide 4
TIME | ACTIVITY | DETAIL
10 mins | STARTER | Interleaved questions
25 mins | 1. Current is affected by potential difference and resistance | The rope loop demonstration is repeated with emphasis on PD and resistance, and a qualitative understanding of these concepts is developed and exercised.
15 mins | 2. Current or potential difference? | Misconception in confusing current and potential difference is explicitly dealt with using examples and counter-examples. Students complete an exercise to check understanding.
10 mins | PLENARY | Question on slide to be answered in books then discussed (see slides for details)
PLAN

## Slide 5
WHAT AFFECTS CURRENT?
Saturday, 02 January 2021

## Slide 6
STARTER
5 mins
1.
What is electric current?
2.
a) Draw a circuit diagram representing the picture.
b) What component could be used to measure the current? Show it on your circuit diagram.
Answer the questions in your book, as fully as possible. You do not need to write the question down.
If you are stuck, leave a gap and move on to the next one.
Notes: 5 minutes to answer, 5 minutes to go through solutions.
Answers could be drawn on the board.
Electric current is the movement of charge/electrons (around a circuit).
a) A series circuit with two batteries, a switch close to the negative end of the batteries, a bulb close to the positive end of the batteries (students may have drawn the batteries the wrong way round: emphasise the convention that the long side of the symbol is the positive end).
b) Ammeter. Check students have used the correct symbol and positioned it in series
RESEARCH NOTES:
4c. Memory: Provide opportunities for pupils to retrieve knowledge they previously learnt. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=26

## Slide 7
1.
Understand current is affected by potential difference and resistance
LEARNING OBJECTIVES
2.
Understand the difference between current and potential difference

## Slide 8
LEARNING OBJECTIVES
2.
Understand the difference between current and potential difference
1.
Understand current is affected by potential difference and resistance

## Slide 9
What affects current?
Notes: Rope model redux
Current is represented by how fast the rope is moving. This can be changed in two ways: how hard the teacher is pushing the rope (be careful not to say how fast!) and how hard the pupil grip is.
Set up the rope loop demonstration as in lesson 1.
1. Increase PD  current increases.
Teacher pushes harder  rope flows faster
(NB take care to refer to the push as ‘harder’ and not ‘faster’ (see misconception).
Highlight that the teacher is transferring more energy to push the rope harder, and the student would feel their hand getting warmer due to increased friction. This is analogous to increased energy transfer at a bulb (greater heating up and glowing) when current increases. How would we see this in a real circuit with a bulb? Bulb would get brighter (because energy is given out as light).
2. Increase resistance  current decreases.
Introduce a second student ‘bulb’ gripping the rope  rope flows slower.
The teacher is pushing the same as before (hard to control, but say you are pushing the same).
Draw pupils’ attention to the fact that the flow decreases everywhere in the circuit all at once (current is still the same everywhere in the circuit).
Mention that the energy put into the circuit by the teacher is instantly ‘shared’ between the two students (each student’s hand experiences less friction and gets less warm than it would if their hand were the only one in the circuit because the rope is passing through it more slowly). How would we see this in a real circuit with bulbs? Bulbs would get dimmer.
RESEARCH NOTES:
1b. Preconceptions: Develop pupils’ thinking through cognitive conflict and discussion – students are likely to express or conceive the powering of the rope in terms of how fast it is being pulled, rather than how hard (see ‘same current’ misconception below). https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=12
3a. Modelling: Use models to help pupils develop a deeper understanding of scientific concepts – models help pupils to link observations to the sub-microscopic and symbolic levels and to build a richer understanding. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=19
4a. Memory: Pay attention to cognitive load – structure tasks to limit the amount of new information pupils need to process – an intuitive understanding of resistance and PD is developed prior to learning quantitative definitions. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=25
Misconceptions research on IOP Spark:
Many pupils think that a battery supplies the same current, regardless of the circuit in which it is used. https://spark.iop.org/many-pupils-think-battery-supplies-same-current-regardless-circuit-which-it-used
Few pupils use the Voltage-Resistance-Current (VRI) model of a series circuit. https://spark.iop.org/few-pupils-use-voltage-resistance-current-vri-model-series-circuit
Many pupils see circuit behaviour as a sequence of causes and effects, rather than seeing the whole circuit as an interacting system. https://spark.iop.org/many-pupils-see-circuit-behaviour-sequence-causes-and-effects-rather-seeing-whole-circuit

## Slide 10
What affects current?
The current in a circuit is determined by the potential difference (push) of the battery, and the resistance of the components in the circuit.
The higher the potential difference, the higher the current.
The higher the resistance, the lower the current.
Potential difference is measured in volts (V).
Resistance is measured in ohms (Ω).
Notes: The current in a circuit is determined by a balance between the push of the battery, and the resistance of the rest of the components – just as with the rope loop the speed of the rope is set by balancing between the teacher’s push and the students’ grip.
In a circuit, the push is called the potential difference of the source. It is measured in volts.
The opposition is called the resistance. It is measured in ohms.

## Slide 11
What affects current?
What we did (rope model) | What it represents | Effect on current | What would would we see?
Teacher pushes harder |  |  | 
Extra student holds rope |  |  | 
Increasing potential difference of battery
Adding an extra bulb to increase resistance
Current increases
Current decreases
Bulb gets brighter
Bulb gets dimmer
Notes: Students should copy this into their books and fill it in as you explain it (included on worksheet if time is short)
How could we tell, in a real circuit, that the current was changing? We would see the brightness of the bulb change.
If the current through a bulb increases, the bulb gets brighter
If the current through a bulb decreases, the bulb gets dimmer

## Slide 12
Which circuit has a brighter bulb?
A
B
All bulbs are identical
Notes: Students have 15s thinking time, then hands-up to vote (Hands up for A, hands up for B, hands up if they will be the same).
Then, cold-call one student to explain the correct answer:
A, because the potential difference is higher (as we have two batteries instead of one), but the same resistance (there is only one bulb). This means the current is higher.
Adapted from www.BestEvidenceScienceTeaching.org Best Evidence Science Teaching project resources

## Slide 13
Which circuit has a brighter bulb?
A
B
All bulbs are identical
Notes: Students have 15s thinking time, then hands-up to vote (Hands up for A, hands up for B, hands up if they will be the same).
Then, cold-call one student to explain the correct answer:
A, because in B the batteries are connected negative-to-negative. This means they are pushing in opposite directions, and the current will cancel out. This means the current is higher in A.

## Slide 14
Which circuit has a brighter bulb?
A
B
All bulbs are identical
Notes: Students have 15s thinking time, then hands-up to vote (Hands up for A, hands up for B, hands up if they will be the same).
Then, cold-call one student to explain the correct answer:
They will be the same, because even though A has twice as much potential difference from having 2 batteries, it also has twice as much resistance as a result of having 2 bulbs. Therefore all bulbs will have exactly the same brightness.

## Slide 15
          TASK 2
5 mins
Read Task 2 on your worksheet carefully.
Join the boxes to explain what happens when components are added.
Draw one line from the added component(s) to what happens. Draw another line to the reason.
Notes: “Over to you”
Adapted from www.BestEvidenceScienceTeaching.org Best Evidence Science Teaching project resources

## Slide 16
Component(s)
          ANSWERS
When it is added
The reason
Notes: Misconceptions
The choice of ‘it is not harder or easier to push current’ as the reason for any prediction suggests the students are thinking of current as determined solely by resistance. (In response to adding one battery it is technically correct, but not the best answer.)
The choice of ‘the batteries push less hard’ to explain dimmer bulbs suggests the battery is able to respond to the situation.
Selection of “Resistance increases  current increases” and the converse in any case indicate a lack of understanding of the inverse relationship between resistance and current
If students have misunderstandings about using the ideas of ‘electrical push’ and ‘resistance’ to explain why adding components to a series circuit reduces the current, it is useful to go back to the rope loop model to challenge thinking and to tease out the correct scientific explanations.
Careful teacher questioning and discussion should quickly lead to an understanding that:
Adding another battery increases the push, so the rope moves faster, there is more friction at the ‘bulb’ and it is brighter.
Adding a bulb anywhere in the loop makes it harder for the battery to push – resistance is increased.
Adding a battery now will push the current harder – and the current can be increased back to what it was before.
Adding a greater number of bulbs slows the current more, but pushing harder with more batteries can get it back to what is was at first.

## Slide 17
Component(s)
          ANSWERS
When it is added
The reason
Notes: Misconceptions
The choice of ‘it is not harder or easier to push current’ as the reason for any prediction suggests the students are thinking of current as determined solely by resistance. (In response to adding one battery it is technically correct, but not the best answer.)
The choice of ‘the batteries push less hard’ to explain dimmer bulbs suggests the battery is able to respond to the situation.
Selection of “Resistance increases  current increases” and the converse in any case indicate a lack of understanding of the inverse relationship between resistance and current
If students have misunderstandings about using the ideas of ‘electrical push’ and ‘resistance’ to explain why adding components to a series circuit reduces the current, it is useful to go back to the rope loop model to challenge thinking and to tease out the correct scientific explanations.
Careful teacher questioning and discussion should quickly lead to an understanding that:
Adding another battery increases the push, so the rope moves faster, there is more friction at the ‘bulb’ and it is brighter.
Adding a bulb anywhere in the loop makes it harder for the battery to push – resistance is increased.
Adding a battery now will push the current harder – and the current can be increased back to what it was before.
Adding a greater number of bulbs slows the current more, but pushing harder with more batteries can get it back to what is was at first.

## Slide 18
Component(s)
          ANSWERS
When it is added
The reason
Notes: Misconceptions
The choice of ‘it is not harder or easier to push current’ as the reason for any prediction suggests the students are thinking of current as determined solely by resistance. (In response to adding one battery it is technically correct, but not the best answer.)
The choice of ‘the batteries push less hard’ to explain dimmer bulbs suggests the battery is able to respond to the situation.
Selection of “Resistance increases  current increases” and the converse in any case indicate a lack of understanding of the inverse relationship between resistance and current
If students have misunderstandings about using the ideas of ‘electrical push’ and ‘resistance’ to explain why adding components to a series circuit reduces the current, it is useful to go back to the rope loop model to challenge thinking and to tease out the correct scientific explanations.
Careful teacher questioning and discussion should quickly lead to an understanding that:
Adding another battery increases the push, so the rope moves faster, there is more friction at the ‘bulb’ and it is brighter.
Adding a bulb anywhere in the loop makes it harder for the battery to push – resistance is increased.
Adding a battery now will push the current harder – and the current can be increased back to what it was before.
Adding a greater number of bulbs slows the current more, but pushing harder with more batteries can get it back to what is was at first.

## Slide 19
Component(s)
          ANSWERS
When it is added
The reason
Notes: Misconceptions
The choice of ‘it is not harder or easier to push current’ as the reason for any prediction suggests the students are thinking of current as determined solely by resistance. (In response to adding one battery it is technically correct, but not the best answer.)
The choice of ‘the batteries push less hard’ to explain dimmer bulbs suggests the battery is able to respond to the situation.
Selection of “Resistance increases  current increases” and the converse in any case indicate a lack of understanding of the inverse relationship between resistance and current
If students have misunderstandings about using the ideas of ‘electrical push’ and ‘resistance’ to explain why adding components to a series circuit reduces the current, it is useful to go back to the rope loop model to challenge thinking and to tease out the correct scientific explanations.
Careful teacher questioning and discussion should quickly lead to an understanding that:
Adding another battery increases the push, so the rope moves faster, there is more friction at the ‘bulb’ and it is brighter.
Adding a bulb anywhere in the loop makes it harder for the battery to push – resistance is increased.
Adding a battery now will push the current harder – and the current can be increased back to what it was before.
Adding a greater number of bulbs slows the current more, but pushing harder with more batteries can get it back to what is was at first.

## Slide 20
Component(s)
          ANSWERS
When it is added
The reason
Notes: Misconceptions
The choice of ‘it is not harder or easier to push current’ as the reason for any prediction suggests the students are thinking of current as determined solely by resistance. (In response to adding one battery it is technically correct, but not the best answer.)
The choice of ‘the batteries push less hard’ to explain dimmer bulbs suggests the battery is able to respond to the situation.
Selection of “Resistance increases  current increases” and the converse in any case indicate a lack of understanding of the inverse relationship between resistance and current
If students have misunderstandings about using the ideas of ‘electrical push’ and ‘resistance’ to explain why adding components to a series circuit reduces the current, it is useful to go back to the rope loop model to challenge thinking and to tease out the correct scientific explanations.
Careful teacher questioning and discussion should quickly lead to an understanding that:
Adding another battery increases the push, so the rope moves faster, there is more friction at the ‘bulb’ and it is brighter.
Adding a bulb anywhere in the loop makes it harder for the battery to push – resistance is increased.
Adding a battery now will push the current harder – and the current can be increased back to what it was before.
Adding a greater number of bulbs slows the current more, but pushing harder with more batteries can get it back to what is was at first.

## Slide 21
LEARNING OBJECTIVES
2.
Understand the difference between current and potential difference
1.
Understand current is affected by potential difference and resistance

## Slide 22
What is the difference between current and potential difference?
Notes: ‘Many students do not understand the difference between current and potential difference. (What is the difference between them in the rope model? A: How fast vs. how hard).’
In a circuit, a battery provides a push. This causes a current to flow.
The battery does not produce current! It just pushes it around, the same way I did not produce the rope – I just pushed it around.
The size of the current depends on the size of the push, but also on the resistance of the rest of the circuit – so even if a battery has a fixed potential difference, we have no way of predicting the size of the current without knowing the rest of the circuit.
[NB rope analogy falls down somewhat after this point, as if it really did behave in the same way as a circuit then if resistance were 0 the rope would move around infinitely fast. You can just say that the speed of the rope is determined BOTH by how hard you push AND how hard the student gripping the rope ‘resists’]
RESEARCH NOTES:
Misconceptions research on IOP Spark: Few pupils can clearly distinguish the ideas of electric current and potential difference. https://spark.iop.org/few-pupils-can-clearly-distinguish-ideas-electric-current-and-potential-difference
1c. Preconceptions: Allow enough time to challenge misconceptions and change thinking – by explicitly pointing out the misconception students are more likely to become aware of whether they hold it. This misconception is further discussed in later lessons. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=13
2c. Self-regulation: Promote metacognitive talk and dialogue in the classroom – It is helpful to discuss wrong ideas and why they’re wrong, as well as why the right idea is right and this helps pupils to examine their preconceptions. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=16
2b. Self-regulation: Model your own thinking to help pupils develop their metacognitive and cognitive knowledge – Model an explanation of what happens in a circuit, making the distinction and relationship between PD and current explicit https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=16

## Slide 23
          TASK 3
10 mins
Read task 3 on your worksheet carefully.
Fill in the gaps to describe what happens in these circuits.
You should only use the terms current and potential difference.
Notes: Adapted from www.BestEvidenceScienceTeaching.org Best Evidence Science Teaching project resources

## Slide 24
          ANSWERS
Circuit with one bulb
The battery has a ………………………………………….. marked on it. This tells me how hard the battery can push ………………………………………….. around the circuit.
To make the bulb brighter I can use a battery with a bigger ………………………………………….. . This will push more ………………………………………….. through the bulb.
Circuit with two bulbs
If I add another bulb, it will make the ………………………………………….. smaller. This is because it is harder to push ………………………………………….. through two bulbs than one.
To make two bulbs as bright as one bulb was, I will need to use a bigger …………………………………………. .
potential difference
potential difference
potential difference
current
current
current
current
2.
Notes: NB Although PD is the best answer for the last space, students may argue that current is correct, because a bigger current does make the bulb brighter. However to make the current bigger they will need to add a bigger PD. This sentence has been deliberately included to provoke further discussion on the detail of the differences between PD and current.
Wrong answers suggest that students are not clearly distinguishing between current and PD.
The next lesson focuses on PD – if students show confusion of current and PD explanations should refer back to the language used in this lesson (current strikes a balance between push and resistance and is determined by both).

## Slide 25
1.
Understand current is affected by potential difference and resistance
LEARNING OBJECTIVES
2.
Understand the difference between current and potential difference
Notes: Review learning objectives

## Slide 26
          PLENARY
10 mins
Three different batteries are used to light a bulb. Exactly the same type of bulb is used each time.
9V
6V
1.5V
  a. Which battery lights the bulb brightest?
  b. How would you explain your answer?
The one on the right
This battery has the greatest potential difference, and the resistance is the same, so current is greatest.
Notes: Adapted from www.BestEvidenceScienceTeaching.org Best Evidence Science Teaching project resources
Students should answer these individually, in full sentences, in their books.
Part a) could be answered by hands-up (Hands up for: left, middle, right, all 3 will be the same), part b) should be answered by cold-calling several students.
Misconceptions
Choosing the 6V battery suggest students are thinking of a battery as the store of electricity, which would be confirmed with an answer such as ‘It is the biggest’ or ‘It holds the most current/charge/electricity/energy’ for the second part.
Students choosing the 1.5V battery and justifying it by saying that it is designed for light bulbs are probably thinking of their own experience of putting cylindrical batteries in torches, rather than the science they have been learning.
Students believing all bulbs will have the same brightness (because the bulb is the same) may be thinking of changing a light bulb at home, where the brightness appears to depend on the bulb used (with no control over PD).
RESEARCH NOTES:
7a. Feedback: Find out what your pupils understand - It is important that you build up an accurate picture of the current understanding of all your pupils https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=38
4d. Memory: Encourage pupils to elaborate on what they have learnt – Elaborative interrogation involves prompting pupils to
generate an explanation for an idea that they have learnt. https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=27
1c. Preconceptions: Allow enough time to challenge misconceptions and change thinking https://educationendowmentfoundation.org.uk/public/files/Publications/Science/EEF_improving_secondary_science.pdf#page=13